## Slide 1: An Analysis of Pedestrian Safety in Cincinnati, Ohio
Patrick McDevitt
Preeti Swaminathan
Joshua Herrera
Raghuram Srinivas
02-Nov-2018

## Slide 2: Cincinnati – Pedestrian Safety Experience
Fatalities : ~12 / year
Accidents w/ Injuries : 350 / year
Total Pedestrian Involved Accidents : 700 / year
Fatalities
Injuries (/10)
Property damage (/100)
# Events
0
20
40
Year
2013
2015
2017
1 / 2

## Slide 3: Cincinnati – Pedestrian Safety Experience
Fatalities : ~12 / year
Accidents w/ Injuries : 350 / year
Total Pedestrian Involved Accidents : 700 / year
Fatalities
Injuries (/10)
Property damage (/100)
# Events
0
20
40
Year
2013
2015
2017

## Slide 4: Pedestrian Accidents – Locations / Severity
Characteristics
  widely dispersed across the city
  heaviest concentration at city center & near east neighborhoods
  National Safety Council estimated cost : $500M / year (all-in)
1 / 2

## Slide 5: Pedestrian Accidents – Locations / Severity
Characteristics
  widely dispersed across the city
  heaviest concentration at city center & near east neighborhoods
  National Safety Council estimated cost : $500M / year (all-in)

## Slide 6: Model Concept – Grid Cell Aggregation
250m
250m
Pedestrian Accidents
Cost factor = Sum(accident * severity)
Event factor = Sum(number events)
Independent Estimators
Non-pedestrian accidents
Pedestrian survey responses
Reported near-misses
Street surface areas
Walk Scores
Fire incidents
Non-emergency service requests
Property values & uses
Public transportation accessibility
cell_id | 530045 | 630027 | 530038 | 
Pedestrian Event Costs | 0.749 | 10.69 | 24.993 | 
sum_cost.y | 973.74 | 1724.687 | 1796.4 | Traffic Accidents
num_events.y | 117 | 196 | 210 | 
num_fire_incd | 0 | 0 | 0 | 
med_sale_res_y | 50,000 | 989,016 | 13,356 | Property Values
med_sale_res_n | 25,600,000 | 12,815,000 | 33,618 | 
med_sale_com_y | 27,413 | 351,822 | 8,303,951 | 
med_sale_com_n | 25,600,000 | 25,600,000 | 25,600,000 | 
med_sale_ind_y | 0 | 444,023 | 0 | 
med_sale_ind_n | 0 | 0 | 0 | 
med_sale_pbo_y | 0 | 0 | 0 | 
med_sale_pbo_n | 0 | 0 | 0 | 
mean_walk_score | 46 | 46 | 68 | Walk Score
min_walk_score | 44 | 44 | 67 | 
max_walk_score | 48 | 48 | 69 | 
num_walk_scores | 0 | 0 | 3 | 
sum_lane_cnt | 206 | 89 | 517 | Street Surfaces
sum_width | 2024 | 907 | 5209 | 
sum_area | 601532 | 122758 | 2745087 | 
num_streets | 43 | 43 | 97 | 
dist | 0.000416949 | 0.000330175 | 0.000343675 | Bus Dist
n_object | 3 | 12 | 6 | 
animals_insects | 36 | 2 | 4 | Non-Emergency Service Requests
building.related | 203 | 38 | 52 | 
construction | 0 | 0 | 0 | 
food | 0 | 6 | 1 | 
others | 124 | 155 | 156 | 
police.property | 4 | 4 | 3 | 
service.complaint | 2 | 1 | 1 | 
street_sidewalk | 11 | 19 | 40 | 
traffic_sig0l | 0 | 3 | 1 | 
trash | 91 | 45 | 64 | 
trees_plants | 8 | 3 | 29 | 
water.leak | 2 | 1 | 1 | 
zoning_parking | 0 | 0 | 1 | 
n_request | 481 | 277 | 353 | 
access | 0 | 0 | 0 | Pedestrian Survey
dblprk | 0 | 0 | 0 | 
dnotyld | 0 | 0 | 0 | 
jywalk | 0 | 0 | 0 | 
lvisib | 0 | 0 | 0 | 
lwfws | 0 | 0 | 0 | 
nobikef | 0 | 0 | 0 | 
noswlk | 0 | 0 | 0 | 
other | 0 | 0 | 0 | 
prkint | 0 | 0 | 0 | 
prkswlk | 0 | 0 | 0 | 
speed | 0 | 0 | 0 | 
vrrlss | 0 | 0 | 0 | 
wlksig | 0 | 0 | 0 | 
xwalk | 0 | 0 | 0 | 
assist | 0 | 0 | 0 | 
bikes | 0 | 0 | 0 | 
drives | 0 | 0 | 0 | 
other.1 | 0 | 0 | 0 | 
walks | 0 | 0 | 0 | 
n_rqst | 0 | 0 | 0 | 
num_near_misses | 0 | 0 | 0 | Misc
All events occurring within same geographic sector aggregated as a common response – predictor data set
1 / 2

## Slide 7: Model Concept – Grid Cell Aggregation
250m
250m
Pedestrian Accidents
Cost factor = Sum(accident * severity)
Event factor = Sum(number events)
Independent Estimators
Non-pedestrian accidents
Pedestrian survey responses
Reported near-misses
Street surface areas
Walk Scores
Fire incidents
Non-emergency service requests
Property values & uses
Public transportation accessibility
cell_id | 530045 | 630027 | 530038 | 
Pedestrian Event Costs | 0.749 | 10.69 | 24.993 | 
sum_cost.y | 973.74 | 1724.687 | 1796.4 | Traffic Accidents
num_events.y | 117 | 196 | 210 | 
num_fire_incd | 0 | 0 | 0 | 
med_sale_res_y | 50,000 | 989,016 | 13,356 | Property Values
med_sale_res_n | 25,600,000 | 12,815,000 | 33,618 | 
med_sale_com_y | 27,413 | 351,822 | 8,303,951 | 
med_sale_com_n | 25,600,000 | 25,600,000 | 25,600,000 | 
med_sale_ind_y | 0 | 444,023 | 0 | 
med_sale_ind_n | 0 | 0 | 0 | 
med_sale_pbo_y | 0 | 0 | 0 | 
med_sale_pbo_n | 0 | 0 | 0 | 
mean_walk_score | 46 | 46 | 68 | Walk Score
min_walk_score | 44 | 44 | 67 | 
max_walk_score | 48 | 48 | 69 | 
num_walk_scores | 0 | 0 | 3 | 
sum_lane_cnt | 206 | 89 | 517 | Street Surfaces
sum_width | 2024 | 907 | 5209 | 
sum_area | 601532 | 122758 | 2745087 | 
num_streets | 43 | 43 | 97 | 
dist | 0.000416949 | 0.000330175 | 0.000343675 | Bus Dist
n_object | 3 | 12 | 6 | 
animals_insects | 36 | 2 | 4 | Non-Emergency Service Requests
building.related | 203 | 38 | 52 | 
construction | 0 | 0 | 0 | 
food | 0 | 6 | 1 | 
others | 124 | 155 | 156 | 
police.property | 4 | 4 | 3 | 
service.complaint | 2 | 1 | 1 | 
street_sidewalk | 11 | 19 | 40 | 
traffic_sig0l | 0 | 3 | 1 | 
trash | 91 | 45 | 64 | 
trees_plants | 8 | 3 | 29 | 
water.leak | 2 | 1 | 1 | 
zoning_parking | 0 | 0 | 1 | 
n_request | 481 | 277 | 353 | 
access | 0 | 0 | 0 | Pedestrian Survey
dblprk | 0 | 0 | 0 | 
dnotyld | 0 | 0 | 0 | 
jywalk | 0 | 0 | 0 | 
lvisib | 0 | 0 | 0 | 
lwfws | 0 | 0 | 0 | 
nobikef | 0 | 0 | 0 | 
noswlk | 0 | 0 | 0 | 
other | 0 | 0 | 0 | 
prkint | 0 | 0 | 0 | 
prkswlk | 0 | 0 | 0 | 
speed | 0 | 0 | 0 | 
vrrlss | 0 | 0 | 0 | 
wlksig | 0 | 0 | 0 | 
xwalk | 0 | 0 | 0 | 
assist | 0 | 0 | 0 | 
bikes | 0 | 0 | 0 | 
drives | 0 | 0 | 0 | 
other.1 | 0 | 0 | 0 | 
walks | 0 | 0 | 0 | 
n_rqst | 0 | 0 | 0 | 
num_near_misses | 0 | 0 | 0 | Misc
All events occurring within same geographic sector aggregated as a common response – predictor data set

## Slide 8: Analysis Method Concept
Grid cell approach
Accumulate experience of candidate features in each cell
Grid cell size : 250m x 250m
  uniform distribution, equidistant edge distances
4196 grid cells
(~80 sq-miles)

## Slide 9: Traffic Accidents (Non-Pedestrian) / Property Values
Accident Density
Costs (NSC model)
Distribution of Property Values (median)
190,000 accidents
426 fatalities

## Slide 10: Transportation / Walk-ability
Public transportation accessibility
distance to nearest bus stop
Walk Score – scale from 0 – 100
  walking distances, block length, intersection density
  calculated every city block
  weighted by population density
Walkable (blue)
Not Walkable (red)

## Slide 11: Random Forest Analysis
Binary & Cost Models implemented
Binary model provides useful results
  ~75% TPR / 20% FPR
Influential factors
  Non-pedestrian involved accidents
  Public transportation accessibility
  Number of service requests for buildings, sidewalk, and vegetation
Potential for Safety Improvement (PSI)
Regions of no events
Regions w/ pedestrian events
1 / 2

## Slide 12: Random Forest Analysis
Binary & Cost Models implemented
Binary model provides useful results
  ~75% TPR / 20% FPR
Influential factors
  Non-pedestrian involved accidents
  Public transportation accessibility
  Number of service requests for buildings, sidewalk, and vegetation
Potential for Safety Improvement (PSI)
Regions of no events
Regions w/ pedestrian events

## Slide 13: Random Forest – Geographic View
Strong contiguity for TP, FP, FN regions
Large surface areas of TN – high model accuracy
PSI identification (FN) perimeter of TP regions
Red = Potential for Safety Improvement
  Widely distributed (consistent with experience of accidents)
  Some at perimeter of city incorporation boundary
Reasonable number of specific regions for further investigation

## Slide 14: Random Forest – Geographic View
Strong contiguity for TP, FP, FN regions
Large surface areas of TN – high model accuracy
PSI identification (FN) perimeter of TP regions
Red = Potential for Safety Improvement
  Widely distributed (consistent with experience of accidents)
  Some at perimeter of city incorporation boundary
Reasonable number of specific regions for further investigation

## Slide 15
Regression Analysis

## Slide 16
Regression Analysis – Cont.

## Slide 17
Variable Analysis
Coefficients Sorted by Significance |  |  |  | 
 | Estimate ($) | Std. Error ($) | t value | Pr(>¦t¦)
Sum Cost of Damage to People in Non-Pedestrian Accidents | 267 | 31.8 | 8.391 | < 2e-16
Unsanitary Food Operations | 39,796 | 8,189 | 4.86 | 1.40E-06
Intercept | 310,397 | 90,519 | 3.429 | 0.00064
Maximum Walk Score | 5,638 | 1758 | 3.207 | 0.00139
Water Leaks and Breaks | -72,140 | 24,776 | -2.912 | 0.00369
Crosswalk Needed | 117,618 | 45,848 | 2.565 | 0.01048
Number of Police Properties | 14,442 | 5,850 | 2.469 | 0.01377
Vehicles Running Red Lights / Stop Signs | 50,332 | 24,291 | 2.072 | 0.03856
Unkempt Flora | 3,998 | 2,158 | 1.853 | 0.06429
Speeding | -62,700 | 34,132 | -1.837 | 0.06658
Parking Close to Intersection | -146,340 | 82,879 | -1.766 | 0.07781
Parking on Sidewalk | 257,246 | 147,334 | 1.746 | 0.08117
Reports of:
  Parking on Sidewalk
  Crosswalks Needed
  Vehicles Running Red Lights / Stop Signs
  Unsanitary Food Operations
  Unkempt Flora
  Speeding
  Water Leaks and Breaks
  Parking Close to Intersection
All changed the estimated pedestrian injury cost by the shown amount.
The number of police properties within an area affected the estimated pedestrian injury cost. The total cost of damage to people involved in non-pedestrian accidents (in millions) affects the estimated cost of pedestrian injuries.
Coefficients below this point are not significant at a p-value of 0.05, but are suggestive of being relevant to the model’s predictive capabilities (p-value <0.1).

## Slide 18: Variable Analysis – Cont. 1/2
Reports of:
  Parking on Sidewalk
  Crosswalks Needed
  Vehicles Running Red Lights / Stop Signs
  Unsanitary Food Operations
  Unkempt Flora
  Speeding
  Water Leaks and Breaks
  Parking Close to Intersection
All changed the estimated pedestrian injury cost by the shown amount.
The number of police properties within an area affected the estimated pedestrian injury cost.
The total cost of damage to people involved in non-pedestrian accidents (in millions) affects the estimated cost of pedestrian injuries.
Coefficients Sorted by Estimate |  |  |  | 
 | Estimate ($) | Std. Error ($) | t value | Pr(>¦t¦)
Intercept | 310,397 | 90,519 | 3.429 | 0.00064
Parking on Sidewalk | 257,246 | 147,334 | 1.746 | 0.08117
Crosswalk Needed | 117,618 | 45,848 | 2.565 | 0.01048
Vehicles Running Red Lights / Stop Signs | 50,332 | 24,291 | 2.072 | 0.03856
Unsanitary Food Operations | 39,796 | 8,189 | 4.86 | 1.40E-06
Number of Police Properties | 14,442 | 5,850 | 2.469 | 0.01377
Maximum Walk Score | 5,638 | 1758 | 3.207 | 0.00139
Unkempt Flora | 3,998 | 2,158 | 1.853 | 0.06429
Sum Cost of Damage to People in Non-Pedestrian Accidents | 267 | 31.8 | 8.391 | < 2e-16
Speeding | -62,700 | 34,132 | -1.837 | 0.06658
Water Leaks and Breaks | -72,140 | 24,776 | -2.912 | 0.00369
Parking Close to Intersection | -146,340 | 82,879 | -1.766 | 0.07781

## Slide 19: Variable Analysis – Cont. 1/2
Reports of:
  Parking on Sidewalk
  Crosswalks Needed
  Vehicles Running Red Lights / Stop Signs
  Unsanitary Food Operations
  Unkempt Flora
  Speeding
  Water Leaks and Breaks
  Parking Close to Intersection
All changed the estimated pedestrian injury cost by the shown amount.
The number of police properties within an area affected the estimated pedestrian injury cost.
The total cost of damage to people involved in non-pedestrian accidents (in millions) affects the estimated cost of pedestrian injuries.
Coefficients Sorted by Estimate |  |  |  | 
 | Estimate ($) | Std. Error ($) | t value | Pr(>¦t¦)
Intercept | 310,397 | 90,519 | 3.429 | 0.00064
Parking on Sidewalk | 257,246 | 147,334 | 1.746 | 0.08117
Crosswalk Needed | 117,618 | 45,848 | 2.565 | 0.01048
Vehicles Running Red Lights / Stop Signs | 50,332 | 24,291 | 2.072 | 0.03856
Unsanitary Food Operations | 39,796 | 8,189 | 4.86 | 1.40E-06
Number of Police Properties | 14,442 | 5,850 | 2.469 | 0.01377
Maximum Walk Score | 5,638 | 1758 | 3.207 | 0.00139
Unkempt Flora | 3,998 | 2,158 | 1.853 | 0.06429
Sum Cost of Damage to People in Non-Pedestrian Accidents | 267 | 31.8 | 8.391 | < 2e-16
Speeding | -62,700 | 34,132 | -1.837 | 0.06658
Water Leaks and Breaks | -72,140 | 24,776 | -2.912 | 0.00369
Parking Close to Intersection | -146,340 | 82,879 | -1.766 | 0.07781

## Slide 20
Terms Explained
Model has underestimated cost
Potential for safety improvement
Model has overestimated cost
Suggested to be high risk

## Slide 21
Terms Explained - Cont.
Model has underestimated cost
Potential for safety improvement
Model has overestimated cost
Suggested to be high risk

## Slide 22
Visualization of Results
Westwood
Clifton
Walnut Hills
Avondale

## Slide 23
Visualization of Results – Cont. 1/2
Westwood
Clifton
Walnut Hills
Avondale

## Slide 24
Visualization of Results – Cont. 2/2
Westwood
Clifton
Walnut Hills
Avondale

## Slide 25
Non-Supervised Learning – K-means Clustering
25
Walk Scores
Commercial Property Values
k-means cluster identification in
t-SNE 2D mapping
Service Requests - trash
Box plot distribution of property values for each cluster
Magnitude distribution of feature
concentrated in 2nd cluster
highest in 2nd cluster

## Slide 26
Non-Supervised Learning – K-means Clustering
26
Walk Scores
Commercial Property Values
k-means cluster identification in
t-SNE 2D mapping
Service Requests - trash
Box plot distribution of property values for each cluster
Magnitude distribution of feature
concentrated in 2nd cluster
highest in 2nd cluster

## Slide 27
Non-Supervised Learning - Observations
27
Blue areas are mostly residential
Green areas have better overall walk score, with a mean score of 54. This falls under "Somewhat walkable, Some errands can be accomplished by walk" of the walk score description.
**** Over-The-Rhine, Mt. Auburn and Central Business District are three neighborhoods with a good walk score, qualifying for "Very walkable" conditions.
Red areas mostly complain about metal trash, while blue area complain about insect and animal related service requests.
Pedestrian-Signal issues like vehicles running stop signs, short walk signals, vehicles that do not yield at crosswalks, and lack of visibility are mainly around Oakely, Clifton, Hyde Park, Madisonville, Pleasant Ridge.
Most Water leaks are predominantly in green.

## Slide 28
Non-Supervised Learning - Observations
28
Blue areas are mostly residential
Green areas have better overall walk score, with a mean score of 54. This falls under "Somewhat walkable, Some errands can be accomplished by walk" of the walk score description.
**** Over-The-Rhine, Mt. Auburn and Central Business District are three neighborhoods with a good walk score, qualifying for "Very walkable" conditions.
Red areas mostly complain about metal trash, while blue area complain about insect and animal related service requests.
Pedestrian-Signal issues like vehicles running stop signs, short walk signals, vehicles that do not yield at crosswalks, and lack of visibility are mainly around Oakely, Clifton, Hyde Park, Madisonville, Pleasant Ridge.
Most Water leaks are predominantly in green.

## Slide 29
Non-Supervised Learning
29
Cluster 0: Blue
Property Type:
Residential
Top Issues:
Animals and Insects
Unkempt Vegetation
Vehicles Running Red Lights and Stop Signs
Cluster 1: Green
Property Type: Commercial
Top Issues:
Speeding
Water Leaks
Heavy Traffic
Vehicles not Yielding
Cluster 2 : Red
Property Type:
Industrial
Top Issues:
Metal Trash
Cars Unable to Find Parking
Lack of Sidewalks
Potholes

## Slide 30
Non-Supervised Learning
30
Cluster 0: Blue
Property Type:
Residential
Top Issues:
Animals and Insects
Unkempt Vegetation
Vehicles Running Red Lights and Stop Signs
Cluster 1: Green
Property Type: Commercial
Top Issues:
Speeding
Water Leaks
Heavy Traffic
Vehicles not Yielding
Cluster 2 : Red
Property Type:
Industrial
Top Issues:
Metal Trash
Cars Unable to Find Parking
Lack of Sidewalks
Potholes

## Slide 31: Conclusions
31
PSI Regions Identified
  ~30 grid cells targeted from random forest binary model
    RF Binary model – 75% TP / 20% FP Rate
    Regression – R2 consistent with published results from other cities
Influential Factors
  Non-pedestrian involved accidents
  Public transportation accessibility
  Number of service requests for buildings, sidewalk, and vegetation
Non-Supervised Learning
  Westwood, Mt. Washington and East End
    Speeding vehicles and non-yielding to pedestrians
  Clifton, Madisonville, Walnut Hills and Mt. Washington
    Construct additional sidewalks and crosswalks
  Over-the-Rhine, Downtown and Clifton
    Increase bike-ability

## Slide 32: Conclusions
32
PSI Regions Identified
  ~30 grid cells targeted from random forest binary model
    RF Binary model – 75% TP / 20% FP Rate
    Regression – R2 consistent with published results from other cities
Influential Factors
  Non-pedestrian involved accidents
  Public transportation accessibility
  Number of service requests for buildings, sidewalk, and vegetation
Non-Supervised Learning
  Westwood, Mt. Washington and East End
    Speeding vehicles and non-yielding to pedestrians
  Clifton, Madisonville, Walnut Hills and Mt. Washington
    Construct additional sidewalks and crosswalks
  Over-the-Rhine, Downtown and Clifton
    Increase bike-ability

## Slide 33: Conclusions
33
PSI Regions Identified
  ~30 grid cells targeted from random forest binary model
    RF Binary model – 75% TP / 20% FP Rate
    Regression – R2 consistent with published results from other cities
Influential Factors
  Non-pedestrian involved accidents
  Public transportation accessibility
  Number of service requests for buildings, sidewalk, and vegetation
Non-Supervised Learning
  Westwood, Mt. Washington and East End
    Speeding vehicles and non-yielding to pedestrians
  Clifton, Madisonville, Walnut Hills and Mt. Washington
    Construct additional sidewalks and crosswalks
  Over-the-Rhine, Downtown and Clifton
    Increase bike-ability